New i915 Modeset Code
Daniel Vetter, Intel OTC
XDC 2012 Nürnberg
[Speaker Notes: meh]

---
[meta: naming things]
- prepare/commit is enable/disable
- encoder is a port
- crtc is a pipe

---
crtc helper assumptions
- simple encoder/crtc split
- independent enable/disable sequence

---
not flexible enough
- cpu eDP PLL
- LVDS pin pair
- Haswell DDI port

---
too flexible
- ->disable called way too often
- ->disable called in different orders

---
new code: simplify dpms
- only old crt supports dpms standy/suspend
- connector drives dpms state
- pipe state is on/off only

---
new code: modeset sequence
- driven by crtc callback
- fixed enable/disable sequence
- encoder callbacks

---
output state staging
- needed for correct disable sequence
- allows better state checking
- ugly part of the conversion

---
hw state readout
- foreign hw state takeover (boot, ...)
- allows hw/sw state cross-checking

---
immediate benefits
- massively reduced modeset state space
- hw state checking is awesome!

---
drm helper api insights
- ->detect logic cleanly separates
- fb helper pokes around in crtc helper internals
- crtc helper modeset semantics are ... fun

---
drm helper wtf moments
- „dpms on“ after modeset
- disabling disconnected outputs
- helper vtables should be typed

---
todo
- drm helper cleanups
- move hpd irq handling into drm/i915
- prep for atomic modeset
- rip out cruft in drm/i915

---
todo: state keeping
- restore responsibility without fbcon
- state keeping for atomic modeset

---
todo: fastboot
- seamless takeover of firmware state
- done: output routing, fb storage
- todo: PLLs, refclocks, panel fitter, interlaced, ...

---
todo: MST DP
- treat DP encoder as shared resources
- or group pipes

---
*BSD ?
sry

---
questions?